## Slide 1: Grocery Shopping Assistant for the Visually Impaired (GroZi)
Ave Joo Byoung Park
(TIES Intern Summer 2010)

## Slide 2: Team Members
Supervisor:
Prof. Serge Belongie
Client:
Dr. John Miller
Visiting Scholar:
Masaaki Kokawa

## Slide 3: Mission Statement
The GroZi project is working to develop a portable handheld device that can “see”, helping the visually impaired navigate more efficiently within difficult environments as well as better locate objects and locations of interest.

## Slide 4: Introduction
Ultimate Goal: coming up with a device that can help the blind do the grocery shopping
Ongoing project since 2007
Consist of three sub-teams
  Computer Vision Sighted Guide
  Wiimote
  Hardware Design

## Slide 5: Goals for this Summer
Studying and proving the concept of finger motion tracking
Running the finger motion tracking simulation by using a Wiimote

## Slide 6: Details of the Simulation
Finger mounted reflective device (e.g. ring)
Wiimote as an IR signal receiver
IR LED array as a light source
Use Wii sensitivity mode

## Slide 7: General Diagram of the Simulation

## Slide 8: Finger Mounted Reflective Ring
Constructed reflective ring prototypes
Materials used:
  Acrylic
  Velcro
  Reflective tape
The prototype design is functional but may be modified in the future

## Slide 9: IR LED Array

## Slide 10: Sensitivity Adjustment Test
Testing with the reflective ring
Testing with hand mirror

## Slide 11: Comments on the Test
The concept is proven and minor adjustments planned for the future
    IR LED emission not strong enough
    The LED emitting angle not wide enough (e.g. 30 degree)
Mirror instead of reflective ring?
    Reflects well  but not suitable
      Reflects the light only at the angle it came in
      Easy to lose the incoming light because of its characteristic

## Slide 12: Conclusion
Use more IR LEDs (approx. 25 to 50 IR LEDs)
Purchase IR LEDs that have wide range of emission (50-60 degree)
Design a curved IR LED array
Start implementing the system in a compact manner

## Slide 13: Reference
Johnny Chung Lee’s Wii Projects
  http://johnnylee.net/projects/wii/
Finger Tracking Wikipedia
  http://en.wikipedia.org/wiki/Finger_tracking

## Slide 14: Acknowledgements
Give thanks to:
Ph D. Serge Belongie
Ph D. John Miller
Chris Cassidy and MAE 3 Design Studio
Rigo Marin and ECE Laboratory Shop
Ph D. Mandy Bratton
Barb Donovan
Zach Salin
Fellow TIES Interns

## Slide 15: Q&A
Any Questions?